## Slide 1
Luminometer
> Measurement
> Status - OK
> Choose calibration
1
POWER ON DEVICE
Luminometer
> Autoexposure
> Timed exposure
> Back to main
Tap top button for autoexposure
Tap/hold middle button
for a timed measurement
ENSURE DEVICE IS UPRIGHT DURING MEASUREMENT!
Luminometer
POWERED OFF
Luminometer
MEASUREMENT IN PROGRESS
A: 1.23 +/- 0.23
B: 2.5 +/- 1.1
Elapsed: 8s Trgt: 30s
2
TAP TOP BUTTON
3
CHOOSE MEASUREMENT TYPE
4
MEASUREMENT IN PROGRESS
Luminometer
Final: Yes
A: 1.23 +/- 0.23
B: 2.5 +/- 1.1
Elapsed: 30s Trgt: 30s
> Clear and go to measurement screen
5
FINAL MEASUREMENT
Tap bottom button after final measurement screen is shown to go back to measurement menu

## Slide 2
1
POWER ON DEVICE
Luminometer
POWERED OFF
2
PLACE DEVICE IN 37C-40C INCUBATOR FOR 30 MINUTES
Luminometer
> Measurement
> Status - OK
> Choose calibration
Luminometer
> Measurement
> Status - OK
> Choose calibration
3
TAP BOTTOM BUTTON
Luminometer
> Restore default calibration
> Custom calibration
> Return to main menu
4
HOLD MIDDLE BUTTON FOR 5s
Luminometer
CAUTION
This will overwrite any existing custom calibration.
Are you sure?
YES – top button
NO – bottom button
5
CONFIRM CUSTOM CALIBRATION
After 30 minutes take the device out of the incubator.

## Slide 3
6
PLACE DEVICE UPRIGHT IN 4C FRIDGE FOR 30 MINUTES
Luminometer
> Measurement
> Status - OK
> Choose calibration
Luminometer
Final: Yes
A: 1.23 +/- 0.23
B: 2.5 +/- 1.1
Elapsed: 30s Trgt: 30s
> Clear and go to measurement screen
7
CALIBRATION
COMPLETE
After 30 minutes the final
measurement screen will be
displayed. Calibration
complete.

## Slide 4
Luminometer
> Measurement
> Status - OK
> Choose calibration
1
HOLD BOTTOM BUTTON FOR 5s
Luminometer
> Yes – top button
---
> No – bottom button
2
TAP TOP BUTTON
*This can be done from any screen (except during a measurement)
3
POWERED OFF
Luminometer
POWERED OFF

## Slide 5
Flip this switch down (AS SHOWN)
Plug in the device with the provided charger. (You should see an orange LED light up inside!)
AFTER the device is powered off, pull the device out of its case
Charging Instructions

## Slide 6
Confirm power off by tapping the TOP button
Wait for the power off screen. After 15 seconds, pull the device out of its housing and flip the power switch off.
Hold the BOTTOM button for 5 seconds from any screen (except during a measurement)
Powering off